## Slide 1: Surface quality prediction for FDM-printed parts using in-process material flow data
Jan Mayera, Tra Bui Thi Thanha , Turgut Caglara , Hendrik Schulza , Omar Ben Lallahoma , Dongxu Lia , Max Niemellaa , Burak Toptasa , Roland Jochema
aChair of Quality Science, Technical University of Berlin, Berlin, 10587, Berlin, Germany

## Slide 2: Agenda
Initial situation and objectives
Methodology and experimental set-up
Results
Conclusion and outlook

## Slide 3: Initial situation and objectives
Reproducability is a big issue in additive manufacturing
Holding a constant quality status is hard in 3D-printing
Micro factories have less connected and „smart“ equipment
Easy-to-use sensors must be involved
Overall:
Pre-controlling the process based on quality criteria is key for effectiveness

## Slide 4: Initial situation and objectives
Use of low cost filament flow sensor to describe the dependency of filament flow and predicted surface quality
Fig.1: Raw filament flow
Fig. 3: Scan of printed parts
Fig. 2: Filament flow Sensor

## Slide 5: Methodology and experimental set-up
Analysis of filament flow with artificially made over extrusion
Data pre-processing with part mapped flow data
Fig. 4: Over extrusion with several factors
0.2
0.4
0.4
0.6
Fig. 5: Flow data processing

## Slide 6: Methodology and experimental set-up
Analysis of filament flow with artificially made over extrusion
Results vary quite a lot indicates certain patterns for different flow rates
Fig. 8: Over extrusion 100 %
Fig. 7: Over extrusion 200 %
Fig. 6: Over extrusion 160 %

## Slide 7: Methodology and experimental set-up
Scan, create point cloud and calcute deviation
In order to create data for each individual work piece, a scan file is processed to identify each printed part and afterwards normalized
Fig. 9: Scan of printed parts
Fig. 10: Create point cloud
Fig. 11: Identify and normlize work pieces

## Slide 8: Methodology and experimental set-up
Scan, create point cloud and calcute deviation
Every identified work piece is then further processed to locate the occured failure
aggregate
Max-Pool
filter
[x1 x2 x3 x4 x5 x6 … ]
[y1 y2 y3 y4 y5 y6 … ]
[max1, max2]
[max1, max2]
sum
Max values
Fig. 12: Failure detection processing

## Slide 9: Methodology and experimental set-up
Usage of Machine Learning to generate accurate forecasts
LSTM, SVR and Linear Regression have both high accuracy and benefits in time series data
Training with labelled data
Prediction of labels

## Slide 10: Results
G-Code
G-Code Modifier
3D-Wall
Flow Analysis
Filament flow
3D point cloud
Scan Analysis
Model data
Model
Surface quality can be well described by filament flow
Only 73 data points were enough to create accurate forecasts
LR and SVR achieve a RMSE of 0.1
LSTM achieves an RMSE of 0.12

## Slide 11: Conclusion and outlook
Factors such as inconsistent data quality, limited extrusion range, and data acquisition time affected the prediction model's performance.
The model's average deviation accuracy of 10% indicates potential, but inherent inaccuracies necessitate further improvements.
Improvements to the prediction model are essential to reduce inaccuracy and increase reliability in predicting surface quality.
The developed application simplifies the surface quality prediction process, and can significantly benefit from additional data.

## Slide 12: Surface quality prediction for FDM-printed parts using in-process material flow data
Jan Mayera, Tra Bui Thi Thanha , Turgut Caglara , Hendrik Schulza , Omar Ben Lallahoma , Dongxu Lia , Max Niemellaa , Burak Toptasa , Roland Jochema
aChair of Quality Science, Technical University of Berlin, Berlin, 10587, Berlin, Germany